## Slide 1: GNRS Assisted Inter-Domain Routing
Suja Srinivasan

## Slide 2: Extending GNRS
Current implementation
      GUID -> NA
Extended to support
  GUID -> Generic Object
Changes
1. Binding object structure
2. Database
3. Network Protocol(insert, update & lookup)

## Slide 3: Binding Object Structure
Value Object
    Value – IP Network Address, GUID, VGUID
    Options – ttl, expiration
Binding Object
    Type – (0, IP Network Address)
    Value Object Array
GUID -> Binding Object

## Slide 4: Database Design
Primary Key: GUID + Type
Secondary Key: GUID
Record: < GUID+Type, GUID, Binding Object >
Search by
    Primary Key : Single Binding Object
    Secondary Key: List of Binding Objects mapped to the GUID
Two databases to ensure faster access to time sensitive bindings
    One will store the network address binding objects alone
    The second will store all the other bindings

## Slide 5: Messages
Insert/Update Request
    GUID
    Binding Object Array
Lookup Request
    GUID
    Type Array
Lookup Response
    Binding Object Array

## Slide 6
Insert/Update Request Payload
0 1 2 3 Octet
+-------+-------+-------+-------+
| GUID |
+-------+-------+-------+-------+
| Number of Mappings |
+-------+-------+-------+-------+ ------------------
| Type |
+-------+-------+-------+-------+
~ ~ Mapping #1
| Type Specific Parsing |
~ ~
+-------+-------+-------+-------+ ------------------
| Type |
+-------+-------+-------+-------+
~ ~ Mapping #2
| Type Specific Parsing |
~ ~
+-------+-------+-------+-------+ -------------------
Notes: 6

## Slide 7
+-------+-------+-------+-------+
| Type |
+-------+-------+-------+-------+
| Number of Addresses |
+-------+-------+-------+-------+ -------------------------
| Len of Addr | Len of Opts |
+-------+-------+-------+-------+
~ ~
| Address |
~ ~
+-------+-------+-------+-------+ Address #1
~ ~
| Options |
~ ~
+-------+-------+-------+-------+ -------------------------
| Len of Addr | Len of Opts |
+-------+-------+-------+-------+
~ ~
| Address |
~ ~
+-------+-------+-------+-------+ Address #2
~ ~
| Options |
~ ~
+-------+-------+-------+-------+ -------------------------
Type Specific – Network Address
Insert/Update Mapping #1 – Network Address
Notes: 7

## Slide 8: Lookup Request Payload
+-------+-------+-------+-------+
| GUID |
+-------+-------+-------+-------+
| Number of Types |
+-------+-------+-------+-------+
| Type #1 |
+-------+-------+-------+-------+
| Type #2 |
+-------+-------+-------+-------+

## Slide 9
Lookup Response Payload
+-------+-------+-------+-------+
| Number of Mappings |
+-------+-------+-------+-------+
~ ~
| Mapping #1 |
~ ~
+-------+-------+-------+-------+
~ ~
| Mapping #2 |
~ ~
+-------+-------+-------+-------+
+-------+-------+-------+-------+
| Type |
+-------+-------+-------+-------+
| Number of Values |
+-------+-------+-------+-------+ -------------------------
| Len of Addr | Len of Opts |
+-------+-------+-------+-------+
~ ~
| Address |
~ ~
+-------+-------+-------+-------+ Address #1
~ ~
| Options |
~ ~
+-------+-------+-------+-------+ -------------------------
| Len of Addr | Len of Opts |
+-------+-------+-------+-------+
~ ~
| Address |
~ ~
+-------+-------+-------+-------+ Address #2
~ ~
| Options |
~ ~
+-------+-------+-------+-------+ -------------------------
Mapping #1 – Network Address
Notes: 9

## Slide 10: Next Steps
Continue with implementation
EIR code understanding

## Slide 11
THANK YOU!